## Slide 1
Motion Planning Library
Library | Advantage | Disadvantage
SBPL Search-Based Planning Library | Efficient Solution | Computataionally expensive Doesn’t scale well to high dimesnsion
OMPL Open Motion Planning Library | Finds feasible collision free path vary fast Computataional efficient than SBPL Scalable due to high dimension | Typically produce jerky/ redundant motion. Paths require post-processing, smoothing, optimization. Completeness and optimality

## Slide 2
Library | Advantage | Disadvantage
CHOMP Covariant Hamiltonian Optimization and Motion Planning | Fluid motion and avoids unusual or awkward joint angles. | Can get stuck in local minima due to gradient. Though theoretically sound, it is difficult to work with in practice. It introduces additional parameters which need to be tuned, and requires multiple random restarts to obtain a successful solution.
STOMP Stochastic Trajectory Optimization for Motion Planning | Requires minimal parameter tuning Does not need cost function gradients. Motor torque is included in cost function | Very low support

## Slide 3
Solver | Method of Solving | No of DOF | Computataional Time
KDL | Numerical | Any | Slower
IK Fast | Analytical | <=6 | Fastest
Track IK | Numerical | Any | Medium
Selected Kinematic Solver: Track-IK
Reason ?
The disadvantage of KDL is that the frequent convergence failures for robots with joint limits and no actions are taken when the search becomes “stuck” in local minima.
The disadvantage of IK Fast is, it can solve only upto 6 DOF.
Track IK is an KDL's enhancement solver which detects and mitigates local minima that can occur when joint limits are encountered during gradient descent.
Kinematic Solver

## Slide 4
Finalised Motion Planner & Kinematic Solver
On top of the analysis done theoretically, different planners in OMPL and Kinematic solvers (Track IK & KDL) were implemented in the robotic arm and were tested in a variety of configuration of robotic arm to find the optimal pair. It was found that the pair: RRT in OMPL and Track-IK solver performed with good accuracy and least amount of computational resources. So these two algorithms were integrated with the control system and tested through simulation.